## Slide 1: BUILDING ON EXPERIENCE 30 years of ‘Alternative Technology’ with a special emphasis on construction
Peter Harper
Centre for Alternative Technology

## Slide 2: WE’LL BE LOOKING AT
Water and sanitation
Energy
Building

## Slide 3: CAT Water Supply System
Reservoir
Toilets
Staff houses
Restaurant
Shop
Filter
Storage tank
UV filter
Ceramic filter
Sand filter
Storage tank
Filtered water
Unfiltered water
Hydroelectricity and irrigation

## Slide 4: WATERLESS TOILETS: NOW A MATURE NICHE TECHNOLOGY?
www.natsol.co.uk

## Slide 5: Constructed wetlands – another mature technology?

## Slide 6: SUMMARY FOR WATER
Whole cycle using on-site sources and sinks
Virtually no energy input, just gravity
Simple plumbing, very few moving parts
Chlorine-free drinking water
Cleaning using simple biological processes, no chemicals
Some nutrient recovery
Positive addition to habitat and biodiversity
Brilliant – but probably a special case

## Slide 7: ENERGY: SOME SUCCESSES, MANY FAILURES

## Slide 8: INTER-SEASONAL SOLAR SPACE HEATING

## Slide 9: AMBITIOUS AND WELL AHEAD OF ITS TIME EVENTUALLY SUCCUMBED TO THE CINDERELLA EFFECT

## Slide 10: MICRO-HYDRO: EXTREMELY RELIABLE, LASTED THE COURSE, COST-EFFECTIVE But invariably a special case

## Slide 11
Water-balanced funicular railway at CAT, Wales
Grid-linked wind turbine
Photovoltaic roof
AUTOMATION IS A KEY FEATURE

## Slide 12
Restaurant
(30kW)
Staff House and Wates
(12kW)
Courses
House
(10kW)
Top Station (8kW)
112m sq. Solar Array
5000l heat store
Underfloor heating in AtEIC
Woodchip/
pellet Boiler 50kW
AtEIC Building (20kW)
IT’S SYSTEMS AS MUCH AS SPECIFIC TECHNOLOGIES: DISTRICT HEATING
Back up LPG Boiler 22kW
Back up LPG Boiler
Back up LPG Boiler 33kW

## Slide 13: ENERGY SOURCES AT CAT The slow defeat of the small as demand outstrips a fixed site Sources listed in ranked order of their contribution
1970s | 1980s | 1990s | 2000s | 2010s
20 P.E. | 40 | 80 | 110 | 150
ELECTRICITY |  | GRID LINKED |  | 
Micro-Hydro, Bottled gas to generator wind PV | Micro-hydro diesel CHP wind Wood gasifier PV | Grid connection Diesel generator Wind Micro-hydro PV | Grid connection Wind Diesel generator Micro-hydro, PV | Failed wood-fuelled CHP Grid connection PV Micro-hydro Wind
HEATING AND COOKING |  |  |  | 
Coal Wood, Solar thermal Bottled gas | Wood, Bulk gas Wind dump Diesel CHP Solar thermal | Wood DH Log stoves Bulk gas Wind dump Solar thermal | Wood DH Bulk gas Log stoves Pellet stoves Solar thermal | Bulk gas Wood DH Log stoves Pellet stoves Solar thermal

## Slide 14: “OFFSETS” Excellent community projects, but even here small scale can be a disadvantage

## Slide 15: BUILDINGS: THE START

## Slide 18: NEXT PHASE Trying everything

## Slide 19: CANADIAN KIT-HOUSE FROM IDEAL HOME EXHIBITION OF 1974

## Slide 20: WATES EARLY SUPER-INSULATED HOUSE 1977 THEN THE BEST-INSULATED BILDING IN THE UK, PERHAPS STILL IS

## Slide 24: EVOLUTION OF SEGAL SYSTEM AT CAT
Lay-friendly self-build
Low-energy self-build
Eco-friendly materials self-build
Use of hardwoods
Large public buildings

## Slide 27: Cliff Railway Stations, CAT Machynlleth
Home-grown oak and recycled pitch-pine frame
Home-grown Larch and Douglas Fir roofing timbers
‘Breathing’ constructions, cellulose insulation

## Slide 28: Autonomous Environmental Information Centre Rammed earth walls Home-grown Ash floors over underfloor heating
Notes: AtEIC Entrance

## Slide 29
THRE HAS BEEN A HARD-TO-MEASURE BUT DISCERNIBLE INFLUENCE IN THE REGION

## Slide 30
Straw
Wool
Wood
Reclaimed wood
Living plants
Earth
NATURAL MATERIALS WITH ‘INDUSTRIAL VITAMINS’

## Slide 31
EARLY INDUSTRIAL
TRADITIONAL LOW-TECH,
LOW-ENERGY/
LOW-CARBON MATERIALS
PRE-INDUSTRIAL
MATURE INDUSTRIAL
META- INDUSTRIAL
HIGH PERFORMANCE
HIGH-CARBON MATERIALS
TRADITIONAL MATERIALS USED AS DECORATION
LOW-CARBON MATERIALS PROVIDE MOST OF THE BULK, POSSIBLY NET-NEGATIVE-C
MODERN MATERIALS USED AS ENABLERS OR ‘INDUSTRIAL VITAMINS’
HIGH PERFORMANCE, BUT ALSO HIGH IMPACT

## Slide 32: ESSENTIALLY A NEW PARADIGM IN BUILDING
CAT’s WISE building is an example
Next?
Buildings designed specifically for carbon-sequestration?
Another story…
THE END